## Slide 1
AutoCAD
AUTODESK
COURSE SLIDES · WSQ
WSQ Technical Drawing with AutoCAD
WSQ Course Code: TGS-2021005538
Skills Framework TSC: Technical Drawing (DSN-TDR-3005-1.11)
Conducted by Tertiary Infotech Academy Pte Ltd · UEN 201200696W
Version v13 · 21 August 2026
© 2026 Tertiary Infotech Academy Pte Ltd. All rights reserved. · www.tertiarycourses.com.sg

## Slide 2
COURSE ADMINISTRATION
Welcome & Housekeeping
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 3
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
• It is mandatory to take the AM, PM and Assessment digital attendance for WSQ-funded courses.
• The trainer/administrator displays the digital attendance QR code from the SSG portal.
• Scan the QR code with your mobile phone camera and submit your attendance.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 4
YOUR TRAINER · TEMPLATE
About the Trainer
TP
Trainer Profile Template
Complete before delivery
NAME
____________________________________________
TITLE / DESIGNATION
____________________________________________
QUALIFICATIONS
____________________________________________
AREAS OF EXPERTISE
____________________________________________
TRAINING & INDUSTRY EXPERIENCE
____________________________________________
CONTACT
____________________________________________
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 5
YOUR TRAINER
About the Trainer
AA
Dr Alfred Ang
Principal Trainer Tertiary Infotech Academy Pte Ltd
ROLE
Principal Trainer, Tertiary Infotech Academy Pte Ltd
SPECIALISATION
CAD, technical drawing and engineering design — AutoCAD, Revit and Fusion 360.
DELIVERS
WSQ courses on technical drawing, design and emerging technologies.
FOUNDER
Founder and lead instructor at Tertiary Infotech / Tertiary Courses.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 6
ICE-BREAKER
Let's Know Each Other
• Your name and organisation / role.
• Your experience with CAD, drafting or design (if any).
• What you want to be able to draw or document after this course.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 7
HOUSEKEEPING
Ground Rules
1
Set your mobile phone to silent mode.
2
Participate actively — no question is stupid.
3
Mutual respect: agree to disagree.
4
One conversation at one time.
5
Be punctual; return from breaks on time.
6
75% attendance is required.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 8
COURSE PORTAL
Login to LMS and Download Course Material
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
8
Log in at lms-tms.tertiaryinfotech.com with your registered email and the OTP sent to your inbox, then open this course to download the slides and Learner Guide.

## Slide 9
COURSE PORTAL · LMS/TMS
Download Course Material
• Log in to the LMS/TMS portal with the account created at registration.
• Portal: https://lms-tms.tertiaryinfotech.com
• Open your course → Course Materials to download the slides and Learner Guide.
• Keep them handy — the final assessment is open book (slides, Learner Guide and approved materials only).
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 10
SCHEDULE
Lesson Plan — 2 Days, 8 hours/day
Day 1
Day 2
• Day 1 — AutoCAD Foundations, Drawing & Modifying Objects
– Digital attendance (AM) · introductions · outcomes
– Topic 1: Getting Started with AutoCAD (Lab 1)
– Topic 2: Technical Drawing with AutoCAD (Labs 2–5)
– Topic 3: Modifying Objects (Labs 6–8)
• Day 2 — Organizing Objects, Design Documentation & Assessment
– Topic 4: Organizing Objects (Labs 9–12)
– Topic 5: Design Documentation (Labs 13–16)
– Course feedback & TRAQOM survey
– Final Assessment: WA (SAQ) + Practical Performance
– Daily timing: 9:30am–6:30pm · 1-hour lunch
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 11
WSQ ALIGNMENT
Skills Framework — TSC
1
TSC Title
Technical Drawing
2
TSC Code
DSN-TDR-3005-1.11
3
Framework
Skills Framework for Design — Technical Drawing, Proficiency Level 3.
4
Coverage
Five abilities (A1–A5) and five knowledge areas (K1–K5) mapped to the five course topics.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 12
SKILLS FRAMEWORK TSC
TSC Abilities & Knowledge
Abilities
Knowledge
• A1: Read and visualise technical drawings according to briefs
• A2: Produce two-dimensional (2D) and three-dimensional (3D) technical drawings based on input from stakeholders
• A3: Create part lists for new design to facilitate technical drawing
• A4: Oversee the development and construction of new designs' prototypes, in collaboration with organisation's production function
• A5: Produce drawings and specifications, that conform to the requirements of relevant standards for submission
• K1: Symbols, standards and conventions used in technical drawings within one's field and region
• K2: Methods of technical drawing by instruments and computer-aided design (CAD) systems
• K3: Types of technical drawings
• K4: Fundamentals of drafting design documentation
• K5: Concepts of information technology (IT) to facilitate the usage of technical drawing software
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 13
WHAT YOU'LL ACHIEVE
Learning Outcomes
1
LO1 — Read
Read and visualize AutoCAD technical drawings.
2
LO2 — Produce
Produce 2D and 3D technical drawings using AutoCAD.
3
LO3 — Part lists
Create part lists using AutoCAD blocks, attributes and tables.
4
LO4 — Document
Create AutoCAD design documentation — text, dimensions, annotation.
5
LO5 — Specify
Produce design specification: layouts, viewports and plotted sheets.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 14
FIVE TOPICS · 16 HANDS-ON LABS
Course Outline
Day 1
Day 2
• Topic 1: Getting Started with AutoCAD (A1, K1)
– AutoCAD user interface
– Workspace settings, navigation and units
• Topic 2: Technical Drawing with AutoCAD (A2, K2)
– Basic AutoCAD operations
– Drawing objects and isometric drawing
• Topic 3: Modifying Objects (A3, K3)
– Working with modifiers: move, copy, trim, arrays…
• Topic 4: Organizing Objects (A4, K4)
– Object properties and layers
– Blocks, attributes and reusable content
• Topic 5: Design Documentation (A5, K5)
– Text, dimensions and part-list tables
– Layouts, printing and outputs
– Annotative techniques
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 15
ASSESSMENT RULES
Briefing for Assessment
• Place phones and other materials under the table or on the floor.
• No photos or recording of assessment scripts.
• No discussion during the assessment.
• Use a black/blue pen for hard-copy assessments.
• No liquid paper / correction tape.
• Scripts are collected when time is up.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 16
FINAL ASSESSMENT
Final Assessment
• Written Assessment (WA) — Short-Answer Questions (SAQ), 1 hour, open book.
• Practical Performance (PP) — produce a dimensioned AutoCAD technical drawing, 1.5 hours, open book.
• Format: Open Book — slides, Learner Guide and approved materials only.
• A minimum of 75% attendance (SSG Digital Attendance record) and a 'Competent' assessment result are required for funding.
• An appeal process is available if required.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 17
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit WA (SAQ) then Practical Performance — open book
▶
4
Submit your answers and DWG file on the LMS
▶
5
Sign the Assessment Summary Record
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 18
CORE CONCEPTS
Technical Drawing & CAD Fundamentals
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 19
K1 · K3 — STANDARDS, CONVENTIONS & TYPES
What is a Technical Drawing?
1
Precise communication
A technical drawing communicates a design's exact geometry, sizes and finishes for manufacture or construction.
2
Standards-based
Symbols, line conventions, projections and dimensioning follow standards (ISO/ANSI) so any reader interprets it the same way.
3
Types
Orthographic multi-view, isometric/pictorial, section, detail and assembly drawings — each answers a different question.
4
CAD advantage
AutoCAD makes drawings precise, editable, layered, reusable and printable at any scale.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 20
METHODOLOGY
The Technical Drawing Workflow
Set up & draw
• Template, units and limits
• Precision aids: snap, ortho, polar
• Draw geometry at 1:1
Organise & refine
• Layers, properties, blocks
• Modify: trim, fillet, array
• Attributes for part data
Document & publish
• Dimensions, text and tables
• Layouts with scaled viewports
• Plot to PDF for submission
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 21
TOPIC 01
Getting Started with AutoCAD
AutoCAD User Interface · Workspace Settings · Navigation · Units
01
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 22
SKILLS FRAMEWORK A1 · K1
Key Concepts — Getting Started with AutoCAD
1
User interface
Application menu, Quick Access Toolbar, ribbon tabs and panels, drawing area, command window and status bar.
2
Workspaces
Drafting & Annotation, 3D Basics and 3D Modeling — task-oriented sets of ribbons, menus and palettes.
3
Model vs paper space
Design at 1:1 in model space; compose scaled drawing sheets in paper-space layouts.
4
Precision aids
Grid and snap, ortho mode, polar tracking, object snaps and dynamic input keep every pick exact.
5
Navigation
Zoom, pan, ViewCube and the wheel mouse move you around a drawing without changing it.
6
Units and limits
UNITS sets the length/angle format and precision; LIMITS frames the working area of the drawing.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 23
USER INTERFACE
AutoCAD User Interface — Application Menu
• The Application button opens the file-level menu: create, open and save drawings.
• Audit, recover and purge a drawing file when it needs repair or cleanup.
• Print or publish a file, and access the Options dialog for system settings.
• Recent documents are listed for quick reopening.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 24
USER INTERFACE
Starting a New Drawing
• Start New Drawing creates a file from the default drawing template (DWT).
• Metric drawings use acadiso.dwt; imperial drawings use acad.dwt.
• The default template is set in the Options dialog.
• Templates carry units, styles, layers and title blocks — start right, draw less.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 25
USER INTERFACE
Ribbon Tabs and Panels
• The ribbon organises tools into tabs (Home, Insert, Annotate, View, Output…).
• Each tab is a set of panels — Draw, Modify, Layers, Annotation and more.
• Panels expand to reveal less-used tools; pin them open while learning.
• Most course commands live on the Home tab's Draw and Modify panels.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 26
USER INTERFACE
Status Bar — Precision Drafting Aids
• The status bar toggles grid, snap, ortho, polar tracking and object snap.
• Ortho constrains the cursor to horizontal/vertical; Polar tracks set angles.
• 2D object snap picks exact endpoints, midpoints, centres and intersections.
• Function keys mirror the toggles: F7 grid · F8 ortho · F9 snap · F10 polar · F3 osnap.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 27
USER INTERFACE
Dynamic Input and the Command Window
• Dynamic input places a command interface beside the cursor as you draw.
• Tooltips show prompts, dimensions and coordinate entry at the crosshair.
• The command window (Ctrl+9) accepts commands and shows every prompt.
• Watch the prompts — AutoCAD always tells you what it expects next.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 28
WORKSPACE
Model Space and Paper Space
• Model space is where you design — always draw at 1:1 real-world size.
• Paper space (layouts) is where you compose scaled sheets for printing.
• The UCS icon shows the origin and orientation of the coordinate system.
• Switch between them with the Model and Layout tabs below the drawing area.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 29
WORKSPACE
Workspaces and the Quick Access Toolbar
• Workspaces group menus, toolbars and ribbons for a task: Drafting & Annotation, 3D Basics, 3D Modeling.
• This course uses Drafting & Annotation throughout.
• The Quick Access Toolbar sits top-left: New, Open, Save, Undo, Plot.
• Right-click any ribbon tool → Add to Quick Access Toolbar to customise it.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 30
NAVIGATION
Navigation — Zoom, Pan and the Wheel Mouse
• The navigation bar provides Pan and the full set of Zoom tools.
• ZOOM (Z): Window, All, Extents, Previous, Scale, Object — know them all.
• Wheel mouse: scroll to zoom, press to pan, double-click to zoom extents.
• Navigation changes your view only — it never moves the geometry.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 31
NAVIGATION
ViewCube and 2D/3D Views
• The ViewCube switches between standard and isometric views of the model.
• Click a face, edge or corner to jump to that view; drag to orbit freely.
• Set Current View as Home to return to a saved orientation.
• In 2D drafting you will mostly stay on the Top view.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 32
SETUP
Drawing Units and Converting Units
• UNITS sets the length type (Decimal, Architectural, Engineering…) and precision.
• Angles default to decimal degrees measured anticlockwise from east.
• This course draws in millimetres with decimal units.
• To convert a drawing's scale: SCALE → All → base 0,0 → factor (e.g. 25.4).
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 33
TOPIC 01 · HANDS-ON
Setting Up a New Drawing
LAB 1
Create and verify a metric drawing environment, compare saved workspace and drafting-setting examples, then open a finished drawing and practise reading it with zoom, pan and ViewCube.
You'll produce
A correctly configured metric drawing saved as DWG, a settings audit, and confident navigation of an existing technical drawing.
Commands: ACADISO template, UNITS, LIMITS, DSETTINGS, WSCURRENT, ZOOM, PAN, ViewCube
Files: lab01-table.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 34
LAB 1 · VERIFY
Setting Up a New Drawing
✅ Check your work
INSUNITS reports millimetres, limits are 420 × 297, Drafting & Annotation is current, the precision-aid audit is complete, and lab01-setup.dwg reopens with the settings intact.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 35
TOPIC RECAP
Recap — Getting Started with AutoCAD
1
Lab 1 — Setting Up a New Drawing
A correctly configured metric drawing saved as DWG, a settings audit, and confident navigation of an existing technical drawing.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 36
TOPIC 02
Technical Drawing with AutoCAD
Basic AutoCAD Operations · Drawing Objects · Isometric Drawing
02
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 37
SKILLS FRAMEWORK A2 · K2
Key Concepts — Technical Drawing with AutoCAD
1
Lines & polylines
LINE draws separate segments; PLINE creates one connected object of line and arc segments.
2
Circles & arcs
Circles by centre/radius or diameter; arcs by combinations of start, centre, end, radius and angle.
3
Rectangles & polygons
RECTANG builds closed rectangular polylines; POLYGON draws 3–1024-sided regular polygons.
4
Ellipses, splines & points
Ellipses from axis endpoints; splines as smooth curves through fit points; points as snap nodes.
5
Construction geometry
Construction lines (XLINE) and rays give infinite reference lines for projecting views.
6
2D isometric drawing
ISODRAFT turns on isometric planes so a flat drawing represents a 3D projection.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 38
DRAWING OBJECTS
Lines
• LINE draws straight segments between picked or typed points.
• Specify the first point, then each next point; every segment is a separate object.
• Combine with object snaps and grid snap for exact geometry.
• Coordinate entry: absolute (100,50) · relative (@50,0) · polar (@50<30).
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 39
DRAWING OBJECTS
Circles and Rectangles
• CIRCLE: centre + radius or diameter; 2P/3P through points; TTR tangent-tangent-radius.
• RECTANG creates a closed rectangular polyline from two corners.
• Rectangle options add chamfered or filleted corners and a set width.
• Use dimensions option (@length,width) for exact rectangle sizes.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 40
DRAWING OBJECTS
Polygons and Ellipses
• POLYGON draws regular polygons of 3–1024 sides.
• Inscribed polygons fit inside the reference circle; circumscribed fit outside.
• ELLIPSE uses two axis endpoints then the half-width of the other axis.
• An elliptical arc is an ellipse with start and end angles.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 41
DRAWING OBJECTS
Arcs, Polylines and Splines
• ARC draws by combinations of start, centre, end, radius, angle and direction.
• PLINE creates one object of connected line and arc segments — switch modes as you draw.
• SPLINE fits a smooth curve through or near a set of fit points.
• Closed polylines are the basis for hatching, areas and 3D operations.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 42
CONSTRUCTION GEOMETRY
Points, Construction Lines and Rays
• POINT places node objects; PDMODE and PDSIZE control how they display.
• Points act as snap nodes — DIVIDE and MEASURE place them along objects.
• XLINE creates infinite construction lines for projecting between views.
• RAY starts at a point and extends infinitely in one direction.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 43
ISOMETRIC
2D Isometric Drawing with ISODRAFT
• A 2D isometric drawing is a flat representation of a 3D isometric projection.
• ISODRAFT switches the crosshairs to the isometric axes (30°/90°/150°).
• F5 cycles the three isoplanes: Top, Right and Left.
• Isocircles (ELLIPSE → Isocircle) draw round features on the active isoplane.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 44
WHAT YOU'LL DO
Hands-On Labs — Technical Drawing with AutoCAD
Labs 2–3
• Creating Lines and Coordinates
• Circles, Rectangles and Polygons
Lab 4
• Polylines, Arcs, Ellipses and Splines
Lab 5
• 2D Isometric Drawing
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 45
TOPIC 02 · HANDS-ON
Creating Lines and Coordinates
LAB 2
Draw the outline of practice drawing EX-1 using the LINE and PLINE commands with absolute, relative and polar coordinate entry, working from its dimensioned drawing sheet.
You'll produce
The completed EX-1 profile drawn to size, matching the supplied solution DWG.
Commands: LINE, PLINE, coordinate entry (@dx,dy · @dist<angle), ORTHO, dynamic input
Files: ex1.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 46
LAB 2 · VERIFY
Creating Lines and Coordinates
✅ Check your work
Your outline closes exactly (LIST shows the final vertex at 0,0) and overlays the solution ex1.dwg with no visible deviation.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 47
TOPIC 02 · HANDS-ON
Circles, Rectangles and Polygons
LAB 3
Complete practice drawing EX-2 by adding circles (centre-radius, diameter, 2P/3P and Tan-Tan-Radius), a rectangle with chamfered/filleted corners and inscribed/circumscribed polygons.
You'll produce
The completed EX-2 drawing with all holes, rectangles and polygons placed to the sheet dimensions.
Commands: CIRCLE (Cen-Rad, 2P, 3P, TTR), RECTANG, POLYGON, object snaps
Files: ex2.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 48
LAB 3 · VERIFY
Circles, Rectangles and Polygons
✅ Check your work
Every circle's centre and radius match the sheet (use LIST), the hexagon has 6 equal sides, and your drawing overlays ex2.dwg cleanly.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
48

## Slide 49
TOPIC 02 · HANDS-ON
Polylines, Arcs, Ellipses and Splines
LAB 4
Draw practice drawing EX-3 combining polylines with arc segments, standalone arcs, an ellipse and a spline, plus construction lines to project feature positions between views.
You'll produce
The completed EX-3 drawing with mixed line/arc geometry drawn as clean, connected objects.
Commands: PLINE (Arc mode), ARC, ELLIPSE, SPLINE, XLINE, POINT/DIVIDE
Files: ex3.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 50
LAB 4 · VERIFY
Polylines, Arcs, Ellipses and Splines
✅ Check your work
The outline is a single polyline (one object when selected), arcs and the ellipse match the sheet dimensions, and no construction lines remain in the final drawing.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 51
TOPIC 02 · HANDS-ON
2D Isometric Drawing
LAB 5
Use ISODRAFT to create a 2D isometric representation of the 3D object supplied in iso-object.dwg, switching isoplanes and drawing isocircles for the round features.
You'll produce
A flat isometric drawing of the 3D object — edges on the three isoplanes plus isocircle holes.
Commands: ISODRAFT, isoplanes (F5), ELLIPSE Isocircle, polar tracking
Files: iso-object.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 52
LAB 5 · VERIFY
2D Isometric Drawing
✅ Check your work
Each face lies on the correct isoplane (edges at 30°/90°/150°), the isocircles read as ellipses aligned to their faces, and the drawing matches the supplied object's proportions.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 53
TOPIC RECAP
Recap — Technical Drawing with AutoCAD
1
Lab 2 — Creating Lines and Coordinates
The completed EX-1 profile drawn to size, matching the supplied solution DWG.
2
Lab 3 — Circles, Rectangles and Polygons
The completed EX-2 drawing with all holes, rectangles and polygons placed to the sheet dimensions.
3
Lab 4 — Polylines, Arcs, Ellipses and Splines
The completed EX-3 drawing with mixed line/arc geometry drawn as clean, connected objects.
4
Lab 5 — 2D Isometric Drawing
A flat isometric drawing of the 3D object — edges on the three isoplanes plus isocircle holes.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 54
TOPIC 03
Modifying Objects
Move · Copy · Rotate · Offset · Mirror · Trim · Fillet · Arrays
03
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 55
SKILLS FRAMEWORK A3 · K3
Key Concepts — Modifying Objects
1
Relocate & duplicate
MOVE, COPY and ROTATE reposition objects from a base point to a second point or angle.
2
Offset & mirror
OFFSET creates parallel copies at a set distance; MIRROR reflects half a symmetric design.
3
Trim & extend
Quick and Standard modes cut objects back to, or extend them to meet, boundary edges.
4
Fillet & chamfer
FILLET rounds a corner with a radius; CHAMFER bevels it with distances or an angle.
5
Arrays
Rectangular, polar and path arrays distribute copies in rows/columns, around a centre, or along a curve.
6
Stretch, scale & explode
STRETCH lengthens with a crossing window; SCALE resizes about a base point; EXPLODE breaks compounds.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 56
MODIFY
Relocating and Duplicating Objects
1
MOVE (M)
Select objects, pick a base point, then the second point — the objects relocate exactly.
2
COPY (CO)
Same flow as MOVE but leaves the original; Multiple mode places copy after copy.
3
ROTATE (RO)
Rotate about a base point by an absolute angle, or use Reference to match geometry.
4
OFFSET (O)
Creates concentric circles, parallel lines and parallel curves at a set distance.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 57
MODIFY
Offset in Practice
• Specify the offset distance, select the object, then click the side to offset to.
• Through mode offsets through a picked point instead of a distance.
• Offset polylines keep their corners; circles offset concentrically.
• Wall outlines, slots and rims are all one offset away from their centreline.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 58
MODIFY
Mirror, Stretch and Scale
1
MIRROR (MI)
Draw half of a symmetric design, then reflect it across a two-point mirror line.
2
STRETCH (S)
Select with a crossing window; endpoints inside move, the rest stay anchored.
3
SCALE (SC)
Resize about a base point by factor — or Reference to hit an exact length.
4
Grips
Select first, then drag grips to stretch/move without any command.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 59
MODIFY
Trim and Extend — Two Modes
Quick mode (default)
Standard mode
• Select the objects to be trimmed or extended, one by one or by dragging
• All visible geometry acts as the cutting/boundary edge
• Fastest for everyday cleanup
• First select boundary edges, press Enter, then select objects to trim/extend
• Press Enter at the first prompt to make everything a boundary
• Precise control for crowded drawings
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 60
MODIFY
Arrays — Rectangular, Polar and Path
• ARRAY creates copies arranged in a pattern — associative by default.
• Rectangular: rows, columns and levels with set spacing.
• Polar: evenly distributes copies around a centre point or axis.
• Path: distributes copies along a line, polyline or curve.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 61
MODIFY
Fillet and Chamfer
• FILLET rounds the corner between two objects with a set radius.
• Enter r (Radius) first to change the current fillet radius.
• CHAMFER bevels a corner using two distances or a distance and angle.
• Radius 0 / distance 0 are quick ways to square off a corner exactly.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 62
MODIFY
Erase, Explode, Break, Divide and Measure
1
ERASE (E)
Remove selected objects — or select first and press Delete.
2
EXPLODE (X)
Break a compound object (polyline, block, array) into components.
3
BREAK / Break at Point
Split lines, open polylines and arcs at one or two points.
4
DIVIDE · MEASURE
Place point nodes at equal counts (DIVIDE) or set intervals (MEASURE).
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 63
WHAT YOU'LL DO
Hands-On Labs — Modifying Objects
Lab 6
• Move, Copy, Rotate and Offset
Lab 7
• Trim, Extend, Fillet and Chamfer
Lab 8
• Mirror, Stretch, Scale and Arrays
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 64
TOPIC 03 · HANDS-ON
Move, Copy, Rotate and Offset
LAB 6
Build practice drawing EX-4 by drawing one feature and then positioning the rest with MOVE, COPY (multiple), ROTATE with reference angle and OFFSET for the parallel profiles.
You'll produce
The completed EX-4 drawing produced with modify commands rather than re-drawing each feature.
Commands: MOVE, COPY (Multiple/Array), ROTATE (Reference), OFFSET
Files: ex4.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 65
LAB 6 · VERIFY
Move, Copy, Rotate and Offset
✅ Check your work
Feature spacings measure correct with DIST, offsets are at the specified distances, and the rotated feature sits at exactly the sheet's angle.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 66
TOPIC 03 · HANDS-ON
Trim, Extend, Fillet and Chamfer
LAB 7
Complete practice drawing EX-5 by trimming overlapping construction geometry, extending short edges to their boundaries, and finishing corners with fillets and chamfers.
You'll produce
A clean EX-5 profile with every corner finished exactly as dimensioned on the sheet.
Commands: TRIM (Quick/Standard), EXTEND, FILLET, CHAMFER, BREAK
Files: ex5.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 67
LAB 7 · VERIFY
Trim, Extend, Fillet and Chamfer
✅ Check your work
No overshooting or dangling segments remain (zoom around the whole profile), and every fillet radius / chamfer distance matches the drawing sheet.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 68
TOPIC 03 · HANDS-ON
Mirror, Stretch, Scale and Arrays
LAB 8
Produce practice drawing EX-6 with mirror, stretch, scale and arrays, then inspect the supplied sawblade drawing to reverse-engineer a production polar-array pattern.
You'll produce
The completed EX-6 drawing plus a verified sawblade polar array with the correct centre, item count, fill angle and associative state.
Commands: MIRROR, STRETCH (crossing window), SCALE (Reference), ARRAYRECT, ARRAYPOLAR
Files: ex6.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 69
LAB 8 · VERIFY
Mirror, Stretch, Scale and Arrays
✅ Check your work
The two halves are symmetric, array counts and spacings match the sheet, the slot length is correct, and you can explain the four defining properties of the sawblade polar array.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 70
TOPIC RECAP
Recap — Modifying Objects
1
Lab 6 — Move, Copy, Rotate and Offset
The completed EX-4 drawing produced with modify commands rather than re-drawing each feature.
2
Lab 7 — Trim, Extend, Fillet and Chamfer
A clean EX-5 profile with every corner finished exactly as dimensioned on the sheet.
3
Lab 8 — Mirror, Stretch, Scale and Arrays
The completed EX-6 drawing plus a verified sawblade polar array with the correct centre, item count, fill angle and associative state.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 71
TOPIC 04
Organizing Objects
Object Properties · Layers · Blocks, Attributes & Reusable Content
04
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 72
SKILLS FRAMEWORK A4 · K4
Key Concepts — Organizing Objects
1
Object properties
Colour, linetype and lineweight — set ByLayer and inspected in the Properties palette (PR).
2
Layers
The primary method of organising a drawing by function; control on/off, freeze/thaw, lock and plot.
3
Grips
Multi-functional grips stretch, move, rotate, scale and copy objects without typing a command.
4
Hide & isolate
Temporarily isolate the objects you are working on and hide the rest of the drawing.
5
Blocks & attributes
Blocks are reusable symbols; attributes attach part numbers and data — the basis of part lists.
6
External references
Xrefs attach another drawing (or PDF underlay) so teams share one live reference file.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 73
PROPERTIES
Object Properties and the Properties Palette
• The Home tab's Layers and Properties panels set the most common properties.
• The Properties palette (PR / Ctrl+1) is the complete list for any selection.
• With nothing selected it shows — and sets — the current defaults.
• Keep colour, linetype and lineweight ByLayer so layers stay in control.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 74
LAYERS
Layers — Organising Every Drawing
• Layers organise objects by function: outlines, hidden lines, centrelines, text, dimensions.
• The Layer Properties Manager creates layers and sets colour, linetype, lineweight and plot.
• All new objects are drawn on the current layer (green tick).
• Off vs freeze: frozen layers are skipped entirely and speed up big drawings; lock to view but not edit.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 75
FOCUS
Hide and Isolate Objects
• Isolate Selected Objects hides everything except your selection.
• Hide Selected Objects removes just the selection from view.
• Both are temporary view states — End Object Isolation restores all.
• Right-click menu or the status-bar lightbulb icon controls isolation.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 76
DIRECT EDITING
Multi-Functional Grips
• Select with no command running and grips appear at defining points.
• Drag a grip to stretch; press Enter to cycle Stretch → Move → Rotate → Scale → Mirror.
• Hover a grip for its multi-function menu (e.g. add vertex, convert to arc).
• Lines, polylines, arcs, dimensions and viewports all expose smart grips.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 77
REUSABLE CONTENT
Blocks, Dynamic Blocks and Attributes
• BLOCK combines objects into a named, reusable symbol inserted with INSERT.
• Dynamic blocks add parameters and actions — one block, many sizes/states.
• Attributes attach data to a block: part numbers, descriptions, quantities.
• ATTDEF defines the tag, prompt and default; DATAEXTRACTION turns attributes into part-list tables.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 78
REUSABLE CONTENT
External References (Xrefs)
• An xref attaches another drawing file into the current drawing — live, not copied.
• The External References palette organises, reloads and repaths every reference.
• Teams share one title block or site plan; edits flow to every host on reload.
• PDFs and images attach the same way as underlays for tracing.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 79
WHAT YOU'LL DO
Hands-On Labs — Organizing Objects
Labs 9–10
• Object Properties and Layers
• Grips, Hide and Isolate
Lab 11
• Blocks, Attributes and Part Lists
Lab 12
• External References and PDF Import
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 80
TOPIC 04 · HANDS-ON
Object Properties and Layers
LAB 9
Create a standards-based layer scheme in lab-table-lesson2.dwg, then audit the supplied office-plan-ground-floor.dwg to see how a larger architectural drawing separates systems.
You'll produce
A layered table drawing where every object is ByLayer, plus a five-layer audit of the office plan covering naming, colour, linetype, lineweight and plot state.
Commands: LAYER (LA), Properties palette (PR), Layer Walk, MATCHPROP, freeze/thaw, lock
Files: lab-table-lesson2.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 81
LAB 9 · VERIFY
Object Properties and Layers
✅ Check your work
Turning each layer off hides exactly its objects, everything in table-layers.dwg reports ByLayer, and the office-plan audit identifies five layers with their intended functions.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 82
TOPIC 04 · HANDS-ON
Grips, Hide and Isolate
LAB 10
Use multi-functional grips on EX-7, then practise isolate, hide, select-similar and end-isolate in the denser new-office-design.dwg without losing or deleting objects.
You'll produce
An edited EX-7 layout plus a saved office-plan view in which the targeted object class was isolated, edited and fully restored.
Commands: Multi-functional grips, grip modes (Enter to cycle), Isolate/Hide Objects, Select Similar
Files: ex7.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 83
LAB 10 · VERIFY
Grips, Hide and Isolate
✅ Check your work
You can stretch, move, rotate and copy with grips alone; after UNISOLATEOBJECTS, the office drawing's object count and layer visibility match the starting state except for your saved edit.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 84
TOPIC 04 · HANDS-ON
Blocks, Attributes and Part Lists
LAB 11
Inspect a reusable block library and a drawing containing dynamic blocks, then define a part-tag block with attributes and prepare its data for the part list.
You'll produce
A BALLOON block with PART_NO / DESC / QTY attributes, plus evidence that one library block and one dynamic-block state can be inserted and edited correctly.
Commands: BLOCK, WBLOCK, DesignCenter, ATTDEF, INSERT, ATTEDIT, dynamic-block grips, DATAEXTRACTION
Files: title-block.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 85
LAB 11 · VERIFY
Blocks, Attributes and Part Lists
✅ Check your work
The library block inserts at the correct scale, the dynamic state changes without exploding, and Data Extraction lists one row per BALLOON with the values you entered.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 86
TOPIC 04 · HANDS-ON
External References and PDF Import
LAB 12
Repair and verify the relative Landscaping_REV1 Xref in the supplied office-layout host, then attach a title block and a PDF underlay and import vector geometry.
You'll produce
A host drawing whose landscaping Xref resolves from the lab folder, with an additional live title-block Xref and an imported PDF geometry sample.
Commands: XREF/ATTACH, External References palette, PDFATTACH, PDFIMPORT
Files: title-block.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 87
LAB 12 · VERIFY
External References and PDF Import
✅ Check your work
Both Xrefs show Loaded, Landscaping_REV1 uses a relative path and survives reopening the folder elsewhere, while PDFIMPORT produces editable AutoCAD objects from the underlay.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
87

## Slide 88
TOPIC RECAP
Recap — Organizing Objects
1
Lab 9 — Object Properties and Layers
A layered table drawing where every object is ByLayer, plus a five-layer audit of the office plan covering naming, colour, linetype, lineweight and plot state.
2
Lab 10 — Grips, Hide and Isolate
An edited EX-7 layout plus a saved office-plan view in which the targeted object class was isolated, edited and fully restored.
3
Lab 11 — Blocks, Attributes and Part Lists
A BALLOON block with PART_NO / DESC / QTY attributes, plus evidence that one library block and one dynamic-block state can be inserted and edited correctly.
4
Lab 12 — External References and PDF Import
A host drawing whose landscaping Xref resolves from the lab folder, with an additional live title-block Xref and an imported PDF geometry sample.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 89
TOPIC 05
Design Documentation
Text · Dimensions · Tables & Part Lists · Layouts, Viewports & Plotting
05
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 90
SKILLS FRAMEWORK A5 · K5
Key Concepts — Design Documentation
1
Text & text styles
Single-line and multiline text; a text style controls font, height and justification centrally.
2
Dimensions
Linear, aligned, angular, radial, diameter, ordinate and arc-length dimensions annotate real sizes.
3
Dimension styles
A named collection of settings — arrowheads, text placement, tolerances — applied consistently.
4
Multileaders & clouds
Multileaders point notes at features; revision clouds flag changed areas for checking.
5
Tables & part lists
TABLE creates row/column data such as bills of materials extracted from block attributes.
6
Layouts & plotting
Scaled viewports on a titled layout sheet, printed with PLOT or published to PDF/DWF.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 91
ANNOTATION
Text and Text Styles
• Multiline text (MTEXT) fills a bounding box; single-line text (TEXT) is quick labels.
• A text style names a collection of settings: font, height, spacing, justification.
• Create styles once (STYLE) and every note updates when the style changes.
• Annotative styles size text automatically to the viewport scale.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 92
ANNOTATION
Dimensions — The Basic Types
• Linear and aligned dimensions measure edges; angular measures between lines.
• Radial and diameter dimensions measure arcs and circles, with centre marks.
• Arc-length and ordinate dimensions cover curved lengths and datum offsets.
• Continue chains dimensions end-to-end; Baseline stacks them from one datum.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 93
ANNOTATION
Dimension Styles
1
What a style controls
Arrowheads, extension lines, text placement, units and tolerances — consistently.
2
Create
DIMSTYLE → New: name it, set fit, text height and precision for your standard.
3
Apply
Set the style current before dimensioning; existing dimensions can be updated.
4
House rule
Never override individual dimension text — fix the style instead.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 94
ANNOTATION
Multileaders and Revision Clouds
• A multileader is an arrowhead, landing line and note text (or block) in one object.
• MLEADER places it; add/remove leader lines and align multiple leaders neatly.
• Revision clouds flag changed areas for checking and approval.
• Draw a cloud by dragging, corner points — or convert an existing closed object.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 95
PART LISTS
Tables and Part Lists
• TABLE creates a compound object of rows and columns from a table style.
• Type into cells like a spreadsheet; formulas and fields are supported.
• DATAEXTRACTION fills a table from block attributes — the bill of materials.
• Tables can link to external Excel data and update both ways.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 96
OUTPUT
Layouts and Viewports
• A layout is the 2D sheet environment: title block, viewports, annotation.
• MVIEW creates layout viewports — windows into model space.
• Set each viewport's scale exactly (e.g. 1:20), then lock it against accidental zooming.
• One model, many sheets: each layout composes its own views and scales.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 97
OUTPUT
Plotting and Printing
• Plot from the layout: choose plotter, paper size, plot area, scale and orientation.
• DWG To PDF.pc3 publishes the standard submission PDF.
• Page setups save the configuration per layout and import between drawings.
• Preview before plotting — check lineweights, scale and the full sheet.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 98
DETAIL
Hatching and Gradients
• HATCH fills enclosed areas with patterns (ANSI31 for sections), solids or gradients.
• Pick an internal point — island detection keeps text and holes clear.
• Scale and angle make adjacent parts read distinctly in section views.
• HATCHEDIT changes an existing hatch; hatches stay associative to their boundary.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 99
WHAT YOU'LL DO
Hands-On Labs — Design Documentation
Labs 13–14
• Text and Text Styles
• Dimensions, Multileaders and Part-List Tables
Lab 15
• Hatching and Detail Finishing
Lab 16
• Layouts, Viewports and Plotting
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 100
TOPIC 05 · HANDS-ON
Text and Text Styles
LAB 13
Annotate the layered table drawing with single-line and multiline text, create and apply text styles for titles and notes, and fill in the title-block fields.
You'll produce
An annotated drawing with consistent TITLE and NOTES text styles and a completed title block.
Commands: TEXT, MTEXT, STYLE, annotative text, SPELL
Files: lab-table-lesson2.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 101
LAB 13 · VERIFY
Text and Text Styles
✅ Check your work
All annotation uses your named styles (none on Standard), the title block is complete, and changing the NOTES style font updates every note at once.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 102
TOPIC 05 · HANDS-ON
Dimensions, Multileaders and Part-List Tables
LAB 14
Fully dimension practice drawing EX-8 with a metric dimension style — linear, aligned, radial, diameter, angular, continue and baseline — add multileader callouts, and create the part-list table from the Lab 11 balloon attributes.
You'll produce
A fully dimensioned EX-8 sheet with leader notes and a parts table (part no · description · qty).
Commands: DIMSTYLE, DIM, DLI/DAL/DRA/DDI/DAN, DCO/DBA, MLEADER, TABLE, DATAEXTRACTION
Files: ex8.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 103
LAB 14 · VERIFY
Dimensions, Multileaders and Part-List Tables
✅ Check your work
Every dimension on the EX-8 sheet is reproduced with the MECH-25 style (no overridden text), leaders land neatly, and the table rows match the balloons one-for-one.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 104
TOPIC 05 · HANDS-ON
Hatching and Detail Finishing
LAB 15
Apply section hatching with controlled boundaries and islands, then compare two supplied landscaping revisions and mark the changed area with a revision cloud and note.
You'll produce
A correctly hatched section view plus a documented landscaping revision showing the changed geometry, revision cloud and concise change note.
Commands: HATCH, gradient fills, boundary/island detection, HATCHEDIT, DWG Compare, REVCLOUD, MLEADER
Files: ex3.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 105
LAB 15 · VERIFY
Hatching and Detail Finishing
✅ Check your work
Hatches do not bleed, adjacent parts use distinct angles, islands remain clear, and the landscaping review identifies every revision with one cloud and one readable note.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 106
TOPIC 05 · HANDS-ON
Layouts, Viewports and Plotting
LAB 16
Audit the supplied new-office-layout.dwg, then compose an A3 layout with a title block, locked scaled viewports and a standards-compliant PDF plot.
You'll produce
A print-ready A3 office layout with two locked viewports, completed title information, verified lineweights and a plotted PDF.
Commands: LAYOUT, PAGESETUP, MVIEW, viewport scale/lock, PLOT, DWG to PDF.pc3
Files: title-block.dwg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 107
LAB 16 · VERIFY
Layouts, Viewports and Plotting
✅ Check your work
Both viewports report their exact scales in the status bar and cannot be zoomed when locked, and the plotted PDF shows the complete titled sheet at A3.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 108
TOPIC RECAP
Recap — Design Documentation
1
Lab 13 — Text and Text Styles
An annotated drawing with consistent TITLE and NOTES text styles and a completed title block.
2
Lab 14 — Dimensions, Multileaders and Part-List Tables
A fully dimensioned EX-8 sheet with leader notes and a parts table (part no · description · qty).
3
Lab 15 — Hatching and Detail Finishing
A correctly hatched section view plus a documented landscaping revision showing the changed geometry, revision cloud and concise change note.
4
Lab 16 — Layouts, Viewports and Plotting
A print-ready A3 office layout with two locked viewports, completed title information, verified lineweights and a plotted PDF.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 109
WRAP-UP
Course Summary & Next Steps
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 110
LEARNING OUTCOMES
What You Achieved
1
Getting started
Navigated the AutoCAD UI, workspaces, units and precision drafting aids.
2
Technical drawing
Produced accurate 2D drawings and isometric views from dimensioned sheets.
3
Modifying objects
Built designs efficiently with move/copy, offset, trim, fillet and arrays.
4
Organizing objects
Structured drawings with layers, blocks, attributes and external references.
5
Design documentation
Dimensioned, annotated, tabulated part lists and plotted submission-ready sheets.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 111
KEEP LEARNING
Recommended Next Courses
1
Architecture Drawing with Revit
WSQ · Tertiary Infotech Academy
2
Product Design with Fusion 360
WSQ · Tertiary Infotech Academy
3
AutoCAD Civil 3D for Infrastructure Design
WSQ · Tertiary Infotech Academy
4
Technical Drawing with AutoCAD Mechanical
WSQ · Tertiary Infotech Academy
5
Technical Drawing with AutoCAD Electrical
WSQ · Tertiary Infotech Academy
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 112
WE'RE HERE TO HELP
Support
• If you have any enquiries during and after the class, contact us:
• Email: enquiry@tertiaryinfotech.com
• Tel: +65 6100 0613
• Website: www.tertiarycourses.com.sg
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 113
BEFORE YOU LEAVE
Cert & TRAQOM Survey (Mandatory)
• Complete the TRAQOM course-quality survey on the LMS — it is mandatory for WSQ funding.
• Your e-certificate is issued on the LMS after you are assessed Competent and the survey is done.
• Portal: https://lms-tms.tertiaryinfotech.com
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 114
ASSESSMENT
Final Assessment
• Written Assessment (WA) — Short-Answer Questions (SAQ), 1 hour, open book.
• Practical Performance (PP) — produce a dimensioned AutoCAD technical drawing, 1.5 hours, open book.
• Open book: slides, Learner Guide and approved materials only.
• Remember to take the Assessment digital attendance (TRAQOM).
• Submit your completed answers and DWG files on the LMS at https://lms-tms.tertiaryinfotech.com.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 115
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit WA (SAQ) then Practical Performance — open book
▶
4
Submit your answers and DWG file on the LMS
▶
5
Sign the Assessment Summary Record
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 116
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
• It is mandatory to take the AM, PM and Assessment digital attendance for WSQ-funded courses.
• The trainer/administrator displays the digital attendance QR code from the SSG portal.
• Scan the QR code with your mobile phone camera and submit your attendance.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 117
HAPPY DRAFTING
Thank You!
You are now ready to read, produce and document technical drawings with AutoCAD.
WSQ Technical Drawing with AutoCAD · TGS-2021005538
© 2026 Tertiary Infotech Academy Pte Ltd
117